STORMWATER MANAGEMENT REQUIREMENTS

FOR

COMPONENT DEVELOPERS

IN

SECTION 24, COMMERCE TOWNSHIP, MICHIGAN

Development Area 1

The DDA has built storm water treatment forebays and constructed stormwater wetlands for detention along the south side of the development area.  The Component Developer will be responsible to provide an overland flood water relief route through the area from Pinewood Industrial Subdivision to Glengary Creek.

Development Area 2

The DDA has built a constructed stormwater wetland for detention along the south side of the development area.  The Component Developer will be responsible for stormwater treatment and providing an overland flood water relief route through the development area from Pinewood Industrial Subdivision to Glengary Creek.  Two storm sewer drains currently run through this area which conveys stormwater from Pinewood Industrial Subdivision.  The drains will be left in place and will be the responsibility of the Component Developer to remove and/or abandon.  The easterly drain will be the responsibility of the Component Developer to reroute and remove or leave in place and fit the development around the drain.  The stormwater from the west drain has been integrated into the Martin Parkway stormwater system and is treated by the existing forebay. This forebay is not sized to handle any treatment from the development area.

Development Area 3

The Component Developer is responsible for stormwater treatment in this development area.  The DDA has been granted a permit by the MDEQ for stormwater detention in the wetland immediately to the east of this area.

Development Area 4

The Component Developer is responsible for stormwater treatment in this development area.  The DDA has been granted a permit by the MDEQ for stormwater detention in the wetland immediately to the west of this area.

Development Area 5

The development area will outlet to the Wal-Mart storm drain system and will be detained in the basin behind Wal-Mart.  The Component Developer is responsible for storm water treatment.

Development Area 6

The Component Developer is responsible for storm water treatment.  The DDA has been granted a permit by the MDEQ for stormwater detention in the wetlands and mitigation areas immediately to the southeast of this area.

Development Area 7

This development area is designed to outlet to the detention basin behind Wal-Mart.  The Component Developer is responsible for storm water treatment discharging to the Wal-Mart basin.

Development Area 8

This development area will outlet to the Martin Parkway storm drain and passes through fore-bays for treatment and then constructed storm water wetlands for detention.

Development Area 9

Storm water treatment in this development area has been provided.  The DDA has been granted a permit by the MDEQ to use the wetlands immediately to the north of this area as a bypass route to the constructed stormwater wetlands for detention.

Development Area 10

The DDA has been granted a permit by the MDEQ to use the wetlands immediately to the north of this area as a bypass route to the constructed storm water wetlands for detention.  The Component Developer is responsible for storm water treatment.

Development Area 11

The Component Developer is responsible for stormwater treatment and storage for this development area.  Currently, no storm drain outlet exists for the area.  A storm drain outlet could potentially be built at Welch Road.  If a storm drain outlet is built, the Component Developer would need to provide detention storage.  If no storm drain outlet is built, the Component Developer would need to provide retention storage.  Storm water detention/retention could potentially be stored on site in the wetland, however, the Component Developer would be responsible to obtain a MDEQ wetland permit for this action.  If no permit is granted, storage would be in the upland area.

Development Area 12

The Component Developer is responsible for storm water treatment for this area before discharging into the existing pond (wetland). The Component Developer is required to obtain a permit from MDEQ to discharge into the pond (wetland). The pond (wetland) is designed to provide required detention volumes. If no permit is granted, detention will be required in the uplands.

Development Guidelines

It is the aspiration of the DDA and Commerce Township to create an economically vibrant area for the development areas while encouraging the use of innovative stormwater management techniques. If these areas utilize environmentally conscience design and quality stormwater management techniques, a reduction in area required for stormwater management may result. Hence, more developable land may become available.